## Slide 1: Tutorial
MOSCAP

## Slide 2
Q. 1) Consider two ‘ideal’ Ti/oxide/p-Si capacitors
φTi = 4.3eV, Eg = 1.1eV, χSi = 4.05eV, φSi = 4.8eV
One uses a low-k (SiO2), the other uses a high-k (HfO2) dielectric, but are otherwise identical. What will be the relation between the threshold voltages using SiO2 and HfO2?

## Slide 3
Q. 2) Consider two ideal MIS capacitors A and B. They differ in only one respect, viz. the semiconductor material in the two cases is different – but only in the relative permittivity (εA > εB). In the depletion regime, for the same applied gate voltage, determine the relation between the surface potentials in the two cases.

## Slide 4
Q. 3) An ideal MOSCAP has VFB = 0. Now, a sheet of positive charge density Qox is introduced within the oxide at a distance xox from the Si/SiO2 interface. Assume the total oxide thickness is tox, what is VFB now?

## Slide 5
Q. 4) The C-V characteristic exhibited by a MOS-C (assumed to be ideal) is displayed
(a)Is the semiconductor component of the MOS-C doped n-type or p-type? Indicate how you arrived at the result.
(b)Draw the MOS-C energy band diagram corresponding to point (2) on the C-V characteristic. (Be sure to include the diagrams for all three components of the MOS-C, show the proper band bending in both the oxide and semiconductor, and properly position the Fermi level in the metal and semiconductor.)
(c)If the area of the MOS-C is 3 x 10-3cm2. what is the oxide thickness (xo)?
(d)Invoking the delta-depletion approximation, determine WT.

## Slide 6
Q. 5) An MOS-C is maintained at T = 300 K, xo = 0.1 µm, and the silicon doping is
NA = 1015/cm3. Compute:
(a) φF in kT/q units and in volts.
(b) W when φS = φF.
(c) ξS when φS = φF.
(d) VG when φS = φF.